## Slide 1
Property Directed Reachability (PDR)
Using Cubes of Non-state Variables With
Property Directed Reachability
PDR is a symbolic model checking algorithm for verifying safety properties.
Ternary Valued Simulation
With Gate Variables
Shifting Time Frames
A new SAT-Based algorithm for symbolic model checking has been gaining popularity. This algorithm, referred to as “Incremental Construction of Inductive Clauses for Indubitable Correctness” (IC3) or “Property Directed Reachability” (PDR), uses information learned from SAT instances of isolated time frames to either prove that an invariant exists, or provide a counter example. The information learned between each time frame is recorded in the form of cubes of the state variables. In this work, we study the effect of extending PDR to use cubes of intermediate variables representing the logic gates in the transition relation. We demonstrate that we can improve the runtime for satisfiable benchmarks by up to 3.2X, with an average speedup of 1.23X. Our approach also provides a speedup of up to 3.84X for unsatisfiable benchmarks.
Ph.D. Candidate, University of Minnesota
Associate Professor, University of Minnesota
John Backes
Marc Riedel
Abstract
SAT Results
The algorithm solves SAT instances representing discrete time frames in isolation.
Variables, Notation and Terms:
Trace Properties
Benchmark | Time States (s) | Frames States | Inv. States | Time Gates (s) | Frames Gates | Inv. Gates | Time Ratio
6s2 | 46.67 | 13 | 601 | 46.35 | 13 | 601 | 0.99
6s34 | 3984.89 | 77 | 2284 | 1053.82 | 89 | 1057 | 0.26
6s6 | 19.19 | 18 | 1709 | 21.59 | 21 | 1796 | 1.13
bj08amba2g3f3 | 1.12 | 10 | 44 | 14.37 | 10 | 48 | 12.83
bjrb07amba10andenv | 2081.17 | 11 | 204 | 2024.49 | 9 | 246 | 0.97
bjrb07amba3andenv | 10.56 | 9 | 103 | 10.07 | 8 | 73 | 0.95
bjrb07amba4andenv | 54.87 | 7 | 78 | 31.6 | 7 | 66 | 0.58
bjrb07amba5andenv | 93.45 | 8 | 130 | 79.5 | 8 | 109 | 0.85
bjrb07amba6andenv | 277.88 | 8 | 160 | 438.81 | 8 | 192 | 1.58
bjrb07amba7andenv | 176.79 | 11 | 148 | 160.12 | 9 | 159 | 0.91
bjrb07amba9andenv | 974.83 | 9 | 253 | 1013.88 | 14 | 185 | 1.04
bob05 | 69.06 | 18 | 407 | 101.86 | 21 | 505 | 1.47
bobcohdoptdcd4 | 84.73 | 17 | 1417 | 51.61 | 13 | 1144 | 0.61
bobsmi2c | 48.03 | 50 | 1121 | 193.33 | 187 | 1183 | 4.03
cmudme1 | --- | --- | --- | 7342.07 | 90 | 7148 | ---
cmudme2 | 4255.06 | 97 | 6197 | 2917.46 | 99 | 4746 | 0.69
eijkbs1512 | 48.11 | 176 | 303 | 31.36 | 161 | 312 | 0.65
eijks382 | 28.02 | 57 | 368 | 34.35 | 69 | 380 | 1.23
eijks420 | 64.07 | 464 | 161 | 67.97 | 501 | 161 | 1.06
eijks444 | 407.75 | 62 | 429 | 237.49 | 61 | 394 | 0.58
eijks526 | 142.32 | 64 | 509 | 80.75 | 62 | 500 | 0.57
intel006 | 23.96 | 11 | 543 | 25.11 | 13 | 615 | 1.05
intel007 | 243.7 | 10 | 1580 | 193.47 | 8 | 1554 | 0.79
intel026 | 2262.39 | 52 | 6504 | 2183.98 | 49 | 6239 | 0.97
intel054 | 239.29 | 19 | 1048 | 305 | 21 | 1129 | 1.27
intel055 | 69.98 | 17 | 309 | 70.03 | 19 | 211 | 1
intel056 | 146.26 | 23 | 835 | 91.82 | 22 | 720 | 0.63
intel057 | 144.43 | 22 | 536 | 134.2 | 20 | 494 | 0.93
intel059 | 62.88 | 18 | 543 | 66.52 | 20 | 536 | 1.06
intel062 | 2095.27 | 28 | 4101 | 2077.67 | 26 | 4909 | 0.99
nusmvguidancep5 | 23.98 | 18 | 292 | 26.35 | 18 | 292 | 1.1
nusmvguidancep7 | 77.49 | 21 | 628 | 78.24 | 21 | 628 | 1.01
nusmvguidancep8 | 19.9 | 22 | 155 | 20.17 | 22 | 155 | 1.01
nusmvguidancep9 | 21.25 | 20 | 154 | 21.25 | 20 | 154 | 1
nusmvreactorp2 | 1093.58 | 172 | 4437 | 2394.32 | 7389 | 7389 | 2.19
nusmvreactorp6 | 1416.97 | 163 | 4390 | 1444.97 | 163 | 4390 | 1.02
pdtpmscoherence | 68.82 | 16 | 1491 | 44.5 | 12 | 1217 | 0.65
pdtpmsheap | 18.72 | 25 | 653 | 11.47 | 23 | 503 | 0.61
pdtpmsretherrtf | 278.97 | 51 | 2510 | 48.65 | 43 | 925 | 0.17
pdtpmsvsar | 25.64 | 11 | 263 | 12.9 | 11 | 260 | 0.5
pdtswvibs8x8p1 | 18.2 | 20 | 867 | 13.45 | 21 | 813 | 0.74
pdtswvqis10x6p1 | 50.05 | 73 | 192 | 35.91 | 66 | 208 | 0.72
pdtswvqis8x8p1 | 108.93 | 56 | 285 | 187.01 | 62 | 339 | 1.72
pdtswvroz10x6p1 | 12.84 | 58 | 73 | 12.99 | 56 | 73 | 1.01
pdtswvroz10x6p2 | 117.03 | 88 | 136 | 105.51 | 76 | 166 | 0.9
pdtswvroz8x8p1 | 13.54 | 50 | 60 | 12.43 | 50 | 64 | 0.92
pdtswvroz8x8p2 | 62.52 | 71 | 183 | 90.46 | 60 | 135 | 1.45
pdtswvsam6x8p3 | 24.84 | 40 | 284 | 24.78 | 39 | 311 | 1
pdtswvtma6x4p2 | 186.35 | 52 | 1537 | 221.31 | 60 | 1758 | 1.19
pdtswvtma6x4p3 | 1006.19 | 58 | 6150 | 1754.36 | 64 | 7837 | 1.74
pdtswvtma6x6p1 | 297.39 | 50 | 1191 | 184.71 | 48 | 1187 | 0.62
pdtswvtma6x6p2 | 1573.62 | 69 | 5944 | 1851.38 | 69 | 7054 | 1.18
pdtswvtms10x8p1 | 107.81 | 16 | 1735 | 97.07 | 15 | 1521 | 0.9
pdtswvtms12x8p1 | 70.52 | 16 | 1531 | 201.81 | 37 | 1625 | 2.86
pdtswvtms14x8p1 | 73.4 | 16 | 1362 | 81.38 | 23 | 1353 | 1.11
pdtvisbakery0 | 30.29 | 32 | 42 | 32.83 | 32 | 42 | 1.08
pdtvisbakery1 | 17.68 | 21 | 47 | 32.17 | 31 | 46 | 1.82
pdtvisbakery2 | 27.42 | 32 | 43 | 25.01 | 27 | 47 | 0.91
pdtvisgoodbakery0 | 24.07 | 27 | 44 | 26.79 | 28 | 40 | 1.11
pdtvisgoodbakery1 | 19.64 | 25 | 46 | 38 | 26 | 55 | 1.93
pdtvisgoodbakery2 | 15.28 | 25 | 43 | 26.12 | 27 | 47 | 1.71
pdtvisns3p00 | 15.51 | 11 | 99 | 23.34 | 11 | 111 | 1.5
pdtvisns3p01 | 12.55 | 12 | 68 | 12.35 | 11 | 82 | 0.98
pdtvisns3p02 | 36.21 | 14 | 125 | 18.3 | 14 | 99 | 0.51
pdtvisns3p03 | 7.14 | 9 | 62 | 15.22 | 12 | 87 | 2.13
pdtvisns3p04 | 20.97 | 13 | 100 | 16.64 | 11 | 97 | 0.79
pdtvisns3p05 | 31.82 | 14 | 126 | 13.44 | 12 | 82 | 0.42
pdtvisns3p06 | 29.23 | 11 | 124 | 20.99 | 11 | 90 | 0.72
pdtvisns3p07 | 19.04 | 16 | 91 | 10.28 | 12 | 84 | 0.54
pdtvistimeout0 | 4649.41 | 35 | 16496 | --- | --- | --- | ---
pdtvisrethersqo4 | 49.12 | 38 | 454 | 31.97 | 38 | 450 | 0.65
pdtvisvending01 | 54.2 | 16 | 1176 | 58.74 | 19 | 1102 | 1.08
Geometric Average | --- | --- | --- | --- | --- | --- | 0.98
Benchmark | Time States(s) | Frames States | Time Gates (s) | Frames Gates | Time Ratio
abp4p2ff | 12.34 | 17 | 6.57 | 15 | 0.53
abp4ptimoneg | 22.46 | 18 | 19.99 | 17 | 0.89
bc57sensorsp0 | 353.59 | 59 | 248.85 | 41 | 0.7
bc57sensorsp0neg | 339.25 | 62 | 353.39 | 55 | 1.04
bc57sensorsp1 | 217.01 | 59 | 550.17 | 73 | 2.53
bc57sensorsp1neg | 595.57 | 63 | 428.22 | 47 | 0.72
bc57sensorsp2 | 468.53 | 69 | 274.03 | 63 | 0.59
bc57sensorsp2neg | 460.64 | 79 | 586.85 | 71 | 1.27
bc57sensorsp3 | 731.42 | 67 | 227.82 | 58 | 0.31
intel017 | --- | --- | 4878.43 | 232 | ---
intel046 | 2274.65 | 68 | 2191.27 | 70 | 0.96
intel045 | 2101.11 | 70 | 1810.71 | 70 | 0.86
intel047 | 1371.72 | 62 | 2643.31 | 69 | 1.93
irstdme4 | 68.67 | 31 | 21.67 | 26 | 0.32
irstdme5 | 19.46 | 26 | 6.46 | 26 | 0.33
irstdme6 | 31.84 | 29 | 17.94 | 28 | 0.56
nusmvtcasp5n | 99.66 | 24 | 78.58 | 24 | 0.79
nusmvtcastp5 | 77.46 | 22 | 67.15 | 23 | 0.87
prodcellp0neg | 77.71 | 60 | 105.54 | 78 | 1.36
prodcellp1 | 155.62 | 72 | 141.58 | 72 | 0.9
prodcellp1neg | 96.87 | 64 | 145.41 | 63 | 1.5
prodcellp2 | 181.08 | 60 | 141.76 | 81 | 0.78
prodcellp2neg | 143.65 | 82 | 114.42 | 62 | 0.8
prodcellp3 | 117.7 | 58 | 102.05 | 56 | 0.87
prodcellp4 | 146.54 | 66 | 143.28 | 75 | 0.98
prodcellp4neg | 162.73 | 80 | 526.8 | 62 | 3.23
Geometric Average | --- | --- | --- | --- | 0.82
Generally better results for satisfiable benchmarks
Some unsatisfiable benchmarks proved faster
A Finate State Machine
(set of primary input variables)
(set of state variables)
(set of initial states)
(transition relation)
(frames containing clauses of state variables)
(set of property states)
The 0th frame contains only the initial states
is an over approximation of states reachable in transitions of the initial states
If a state is not blocked in some frame, then it is not blocked in the next frame either
Every state in the next frame can be reached in one transition from the current frame
The property is satisfied in every frame except the last frame
Blocking Phase:
Find:
Recursively block cubes such that:
Propagation Phase:
If: is unsatisfiable, then cube is blocked in frame
Why Use Cubes of Gate Variables?
x0,x1,x2,x3 | g0,g1 | x4
0000 | 01 | 1
0011 | 01 | 1
0110 | 10 | 1
1100 | 01 | 1
Three cubes in terms of x0,x1,x2,x3 can by blocked by one cube in terms of g0,g1!
Sort the variables in ascending by logic level, set .
If , then return . Else, for the th variable in , if is state variable: go to 4. else, go to 3.
If the value of can be determined to be 1 or 0 (not ) by its fanins, then remove from and go back to 2. Otherwise go to 4.
Set to and simulate the transition relation. If no variable in evaluates to , then remove from and proceed to step 2. Otherwise, set back to its original value, re-simulate the transition relation, increment , and proceed to 2.
UNSAT Results
The ternary valued simulation run twice:
  Once with gate variables
  Once with state variables
In the first pass, the gate cube is reduced.
  Variables are set to is by the logic level and by priority
  Priority increases if unable to be removed from the cube;
In the second pass, the state cube is reduced
  Order in which cube variables are set to is fixed
At the end of both passes, whichever cube is smaller (containing fewer literals) is returned.
is an undefined value (possibly 0 or 1)
Experiment
Original Transition Relation
New Transition Relation
Gates g0,g1,g2,g3 have only state variables in their cone of influence (COI)
Gates g0,g1,g2,g3 have only state variables in their cone of influence (COI)